## Slide 1
1 · CONTEXT
What Is an IoT Network?
FEEC · UNICAMP
Everyday objects that sense, decide, and act — connected through a gateway to cloud services.
Things — sensors & actuators
constrained · cheap · wireless
Camera
Motion sensor
Smart lock
Thermostat
Speaker
Wearable
Zigbee · BLE
Wi-Fi
Gateway / Hub
aggregates traffic · bridges protocols
MQTT · HTTP
Cloud services
analytics · dashboards · remote control
telemetry flows up · commands flow down — every hop is network traffic
Sense → decide → act
The physical world sits inside the control loop — a hijacked device has physical consequences.
MCU-class hardware
Kilobytes of RAM, battery budgets — no room for antivirus or endpoint agents.
Heterogeneous, always on
Dozens of vendors and protocols — and every one of them has a path to the Internet.
⇒ Keep this picture in mind: everything is reachable over the network — almost nothing defends itself.
Notes: SLIDE-PONTE (~70 s). Antes de falarmos de vulnerabilidades, vamos concordar sobre o que é, concretamente, uma rede IoT. São objetos do cotidiano — câmeras, sensores de presença, fechaduras inteligentes, termostatos, caixas de som, vestíveis — equipados com sensores, um pouco de computação e uma interface de rede. A organização típica tem três camadas. Na borda, as “coisas”: dispositivos restritos, baratos e sem fio, que sentem e agem sobre o mundo físico. No meio, um gateway ou hub, que agrega o tráfego e traduz protocolos — Zigbee, BLE e Wi-Fi do lado dos dispositivos; MQTT e HTTP sobre a Internet do outro lado. E na ponta, os serviços de nuvem: análise, painéis e controle remoto. A telemetria sobe, os comandos descem — e cada salto desse caminho é tráfego de rede. Três características definem essas redes e importam para segurança. Primeira: o mundo físico está dentro do laço de controle — um dispositivo comprometido tem consequência física, não apenas digital. Segunda: o hardware é classe microcontrolador — kilobytes de RAM e orçamento de bateria; não há espaço para antivírus nem agente de endpoint. Terceira: o conjunto é heterogêneo e está sempre conectado — dezenas de fabricantes e protocolos, todos com um caminho até a Internet. Guardem esta imagem: cada elemento aqui é alcançável pela rede — e quase nenhum consegue se defender sozinho. É exatamente isso que o próximo slide quantifica.